Designator	Value	Description	Quantity

C22	100pF	Ceramic cap size 0805	1
C23, C24	100nF	Ceramic cap size 1206 C1206C104K1RACTU	2
C25	22pF	Ceramic cap size 0805	1
FB1, FB2	40mR, 3A 25%	0805, 60O, 3A, 25% SMT	2
J5		3.5mm Jack 4-pole with normally closed switches	1
J6		3.5mm Jack 4-pole with normally closed switches	1
L1	2.2uH	Shielded Power Inductor 2.2 uH 20% 2.2 A 50.4 mohms 3.11 A (sat) 60MHz 4018: 4x4x1.8mm	1
Q1		Dual N-channel Enhancement mode power MOSFET	1
Q2		MJD210 PNP BJT transistor DPAK (decawatt) 5A dc	1
Q6		65 V, 100 mA PNP general-purpose transistor	1
R1	150K	Res size 0805 SMD mounting, low power Yageo-RC0805FR-07150KL	1
R8	1.2K	Res size 0603 SMD mounting, low power	1
R14, R17	1M	Res size 0805 SMD mounting, low power. Yageo-RC0805FR-071ML	2
R23, R24	220	Res size 0603 SMD mounting, low power	2
R26, R27, R28, R29	150	Res size 0603 SMD mounting, low power	4
R36	22K	Res size 0603 SMD mounting, low power	1
RT1	10K	NTC THERMISTOR 10K for solding a cable from the battery NTC	1
U1		1.0MHZ, 2A STEP-DOWN DC-DC BUCK CONVERTER, with latch-off protection	1
U2	LDO 1.8V, 80mA	Fixed output lowdropout linear regulator. 1.8 V 80 mA	1
U6		LMV358IDGKR Dual OpAmp; low voltage rail to rail opamp; 2.7V to 5V Vss; ESD protection; MSOP-8 Package.	1
U10		HX711 load cell amplifier	1
U11		TPD3S014TDBVRQ1 ESD prot. & current limit	1
C1, C14, C34	47pF	Ceramic cap size 0805	3
C2, C8, C13, C15, C17, C18, C20, C21, C27, C30, C31, C32, C33, C35, C37, C39, C40, C41, C42	100nF	Ceramic cap size 0805	19
C3, C16, C26, C29, C36, C38	10uF	Ceramic cap size 0805	6
C5	27pF	Ceramic cap size 0805	1
C4, C6, C7, C9, C12, C43	22uF	Ceramic cap size 0805 CC0805MKX5R6BB226 Yageo MLCC 22uF 10V 20% X5R	6
C10, C11, C19	1uF	Ceramic cap size 0805	3
C28	470pF	Ceramic cap size 0805	1
D2, D3, D4, D5, D12, D13		SURFACE MOUNT FAST SWITCHING DIODE	6
D1, D6, D8, D10		Low power LED color Green	4
D7, D9, D11		Low power LED color Red	3
J1		USB-MINI-B Female, Manufacturer PN/ID: 10033526-N3212LF	1
J2, J3		BNC coaxial female connector	2
J4		ILI9341 TFT LCD Jumper pin headers., plus SD card reader pins	1
MCU1		- Transceiver; 802.11 b/g/n _Wi-Fi, WiFi, WLAN_, Bluetooth Smart Ready 4.x Dual Mode For Use With ESP-WROOM-32	1
Q3, Q4			2
Q5		PMOS BSS84AK	1
R18, R21, R22	4.7K	Res size 0603 SMD mounting, low power	3
R3	33K	Res size 0805 SMD mounting, low power	1
R4, R5, R25	0R	Res size 0603 SMD mounting, zero-ohm 0R Yageo RC0603JR-070RL	3
R9, R10, R11, R12, R13, R35, R37, R38, R39, R40	10K	Res size 0603 SMD mounting, low power	10
R2, R6, R33, R34	100R	Res size 0603 SMD mounting, low power	4
R7, R15, R16	1K	Res size 0603 SMD mounting, low power	3
R19	1.5K	Res size 0603 SMD mounting, low power	1
R20	0.2R	Res size 1206 SMD mounting, high power, shunt, current sense.	1
R30, R31, R32	100K	Res size 0603 SMD mounting, low power	3
S1		SWITCH Multidirection Slide Push Button SMD TS-003	1
S2, S3, S4		Generic 2 pin button	3
U3		DW01A One cell Li-Po/Li-ion Battery protection IC	1
U4		1A Standalone Linear Li-lon Battery Charger with Thermal Regulation in SOP-8	1
U5		Very low capacitance ESD protection	1
U7		LTC4060EFE	1
U8		Zero-Drift, Bi-Directional CURRENT/POWER MONITOR with I2C. SOIC-8 (D) Package	1
U9		USB to serial chip CH340C, integrated oscillator.	1